## Slide 1: Dr. Sunirmal Khatua
Visvesvaraya Young Faculty Fellow, Govt. of India
Assistant Professor, University of Calcutta
Presented By
Cellular Networks : GSM(2G)
Notes: We celebrate Christmas to remember the birth of Jesus Christ

## Slide 2
Useful Spectrum

## Slide 3
Radio Spectrum

## Slide 4
Constraint of Frequency in a Spectrum

## Slide 5
Frequency Allocation in Cellular Networks
GSM 900 uses 2 Frequency Bands of 25MHz.
  890-915MHz for UPLINK and 935-960 MHz for DOWNLINK
  Each Band provides 125 Carrier of 200KHz each. 1 Carrier is provided as a Guard Channel
  between GSM and Other Bands.

## Slide 6
Reuse the Frequencies
GSM 900 uses 2 Frequency Bands of 25MHz.
  890-915MHz for UPLINK and 935-960 MHz for DOWNLINK
  Each Band provides 125 Carrier of 200KHz each. 1 Carrier is provided as a Guard Channel
  between GSM and Other Bands.
Cluster
1 set of Frequencies

## Slide 7
Reuse the Frequencies
GSM 900 uses 2 Frequency Bands of 25MHz.
  890-915MHz for UPLINK and 935-960 MHz for DOWNLINK
  Each Band provides 125 Carrier of 200KHz each. 1 Carrier is provided as a Guard Channel
  between GSM and Other Bands.
Cluster
1 set of Frequencies
Starting from any cell A, move i cells along one direction.
Turn anticlockwise 60 degrees, then move j cells in the direction
Assign the same frequency to this cell
Starting from A , repeat for another direction, until all directions are covered.
Frequency Reuse Algorithm
Note : i and j determines the cluster size, N
here N = 7, i = 2, j = 1

## Slide 8
Reuse the Frequencies
Starting from any cell A, move i cells along one direction.
Turn anticlockwise 60 degrees, then move j cells in the direction
Assign the same frequency to this cell
Starting from A , repeat for another direction, until all directions are covered.
Frequency Reuse Algorithm
Note : i and j determines the cluster size, N
here N = 7, i = 2, j = 1
N = 4, i = 2, j = 0

## Slide 9
Relation among i, j and N
Reuse Distance : D2= 3R2(i2 + j2 + ij)
Cell Area : 3 √ 3/2 R2
Cluster Area : √3/2 D2
Cluster Size N=Cluster Area / Cell Area:
N=i2 + j2 + ij, valid N = 1,3,4,7,12,…
R
L
L = √3/2 . R
j
i
D
MDR = B . Log(1+SNR)

## Slide 10
Other Approaches to Increase Capacity
Adding new channels
Frequency borrowing
Cell Splitting
Cell Sectoring

## Slide 11
Second Generation Cellular Networks : 2G
Mobile Station (MS)
    Mobile Equipment (ME)
    Subscriber Identity Module (SIM)
Base Station Subsystem (BSS)
    Base Transceiver Station (BTS)
    Base Station Controller (BSC)
Network Switching Subsystem(NSS)
    Mobile Switching Center (MSC)
    Home Location Register (HLR)
    Visitor Location Register (VLR)
    Authentication Center (AUC)
    Equipment Identity Register (EIR)
Cluster
1 set of Frequencies
MDR = B . Log(1+SNR)
D2= 3R2N

## Slide 12
Call Setup in 2G
PSTN
calling
station
GMSC
HLR
VLR
BSC
BSC
BSC
MSC
MS
1
2
3
4
5
6
7
8
9
10
11
12
13
16
10
10
11
11
11
14
15
17
1: Calling a GSM subscriber
2: Forwarding call to GMSC
3: Signal call setup to HLR
4, 5: Connect with current VLR
6,7: Forward to responsible MSC
8, 9: get current status of MS
10, 11: paging of MS
12, 13: MS answers
14, 15: Security checks
16, 17: Set up connection
Mobile Terminated Call
PSTN
GMSC
VLR
BSC
MSC
MS
1
2
6
5
3
4
9
10
7
8
1, 2: Connection request
3, 4: Security check
5-8: Check resources (free circuit)
9-10: Set up call
Mobile Originated Call

## Slide 13
GSM Authentication
Encrypt
RAND
Ki
128 bit
128 bit
SRES* 32 bit
Encrypt
RAND
Ki
128 bit
128 bit
SRES 32 bit
SRES* =? SRES
SRES
RAND
SRES
32 bit
mobile network
SIM
AC
MSC
SIM
Ki: individual subscriber authentication key SRES: signed response

## Slide 14
GSM Physical Channel
GSM = FDMA + TDMA
GSM 900 uses 2 Frequency Bands of 25MHz.
  890-915MHz for UPLINK and 935-960 MHz for DOWNLINK
  Each Band provides 125 Carrier of 200KHz each. 1 Carrier is provided as a Guard Channel between GSM and Other Bands.
Each Carrier uses 8 Time Slots (TS) TDMA
Thus GSM provides 8 * 124 Full Duplex Channel.
Each such Channel (Carrier + TS) is called a Physical Channel.

## Slide 15
GSM Frame Structure

## Slide 16
GSM Logical Channel
Speed of TCH/F = 24x2x57 bits in 120ms = 22.8kbps
Effective Speed = 13kbps after channel encoding with FEC
For Half rate TCH, FN 12 is signaling and FN 25 is idle for first User while FN 25 is signaling and FN 12 is idle for second User
For Full Rate TCH, FN 12 will be used for signaling while FN 25 is idle

## Slide 17
GSM Logical Channel

## Slide 18
GSM Logical Channel
  Slow Associated Control Channel (SACCH) – power control and timing information in the downlink while received signal strength and link quality reports in the uplink.
  Fast Associated Control Channel (FACCH) – used to transmit urgent messages e.g. handover. It is sent by steeling 57 bits within a TCH slot.
  Standalone Dedicated Control Channel (SDCCH) – used along with SACCH to send and receive messages.

## Slide 19
GSM Logical Channel

## Slide 20
GSM Logical Channel
  Communicated in TS 0 of each of the 51 Multiframe

## Slide 21
GSM Logical Channel

## Slide 22
Questions?
Thank You